## Slide 1: Low-Band Receive Antennas
How to hear that great DX that you’re missing on 40, 80 and 160!
Al Penney
VO1NO / VE3

## Slide 2: Tonight’s Topics…
Introduction
Receiving Basics
RX Loops
Elongated Terminated Loops
  EWE Antenna
  Flag Antenna
  Pennant Antenna
  K9AY Loop
Beverages
Notes: Doug VE3XK was the person who persuaded me to prepare a presentation on receive antennas. I found a picture of Doug when he was a young Ham….

## Slide 3
Notes: This is Harold H. Beverage at his Amateur Radio Station. Possibly at the University of Maine around 1915

## Slide 4: Why do we need separate TX and RX antennas?
Because, they have different requirements:
  TX antennas need to deliver strongest possible signal into target area compared to other antennas.
  Efficiency and gain are most important factors.
  RX antennas need to have best Signal to Noise Ratio (SNR) – gain and efficiency are not necessary.
Notes:         For a transmit antenna, we want maximum possible field strength in a given direction (or directions) at the most useful elevation (wave) angles. We cannot tolerate unnecessary power loss in a transmit antenna, because any amount of transmitting loss decreases signal-to-noise ratio at the distant receiver. Antenna efficiency is an important issue for transmitting. It is obvious that for a given elevation angle and direction the highest gain antenna will deliver the strongest signal to the target area. We really do not care if we are being heard in other directions (areas) or not, we are only interested in the target direction.
        A receiving antenna on the other hand has a different design priority. The goal is obtaining a signal that can be read comfortably, which means having the minimum possible amount of QRM and noise. The important issue when receiving is signal-to-noise ratio (S/N). The receiving antenna providing the best performance can and will be different under different circumstances, even at the same or similar locations. There is no such thing as a universal “best low-band receiving antenna.”
        An example might better illustrate the concept:

## Slide 5
Antenna A
Antenna B
(+3dB gain vs Antenna A)
Is Antenna B a better TX
Antenna than Antenna A?
Diagrams from ON4UN’s
Low Band DXing

## Slide 6
Single 720-foot Beverage.
Two 720-foot Beverages.
Spaced 70 feet apart.
Diagrams from ON4UN’s
Low Band DXing

## Slide 7
Gain single Beverage: -11.2 dBi
Gain two Beverages (70-ft sp): -8.2 dBi
So, a pair of Beverages (with 70-ft spacing) has 3 dB gain over a single Beverage.
But, has anything actually been gained in terms of Signal/Noise ratio?

## Slide 8: NO – nothing has been gained!
The pattern is still practically identical
  Front/Back is the same
  Front/Side is within 0.47dB
Unwanted noise is external to the antenna. Because the directivity of the two antenna systems is the same, the Signal/Noise ratio is exactly the same for both.
We must use Directivity when comparing RX Antennas, not gain.
Notes: There are a few things we have to keep in mind:
1.) If noise is not evenly distributed (which is often the case) performance will depend on the gain difference between desired signal direction (azimuth and elevation) to gain in the direction of noise(s). A 20dB null on the noise compared to gain in the desired signal direction will actually improve S/N ratio by 20 dB, if the noise from the null direction totally dominates all other noises.
2.) If noise arrives primarily from the same direction and angle as the desired signal (and assuming polarization of signals and noise is the same), there will be no S/N improvement.
3.) If noise originates in the near field of the antenna, all bets are off. Anything can happen.

## Slide 9: How much Negative Gain can we tolerate with RX antennas?
Modern receivers are very sensitive.
If you can easily hear an increase in background noise when switching from a dummy load to an RX antenna under quietest conditions, then gain is sufficient.
Minus10 to minus 20 dBi Gain is generally fine for most occasions.

## Slide 10: Noise
The sum of all unidentified signals (thunderstorms, man-made, cosmic etc.).
Requires its own presentation!
RX antennas reduce noise through:
  Directivity
  Null placement
  Noise canceling devices
  Height
Notes:         While often attributed to charged particles (such as water droplets) hitting an antenna, most precipitation static is actually caused by intense electric field gradients in the area surrounding the antenna. Such conditions commonly appear during inclement weather, when movement of particles or moisture causes concentrated areas of charges. The strong electric fields are responsible for noise-producing corona discharges. The noise comes from low-current corona discharges from sharp or protruding objects. (St. Elmo’s Fire)
        Using an antenna at a lower height reduces corona current—The electric-field gradient is smaller close to the wide smooth surface of the earth. Vertical antennas are particularly sensitive to precipitation static; they have pointed ends protruding upwards towards the oppositely charged sky.
        Beverages on the other hand, being near earth, will have fewer corona discharge problems. They also have low surge impedances. This means the low-current high-voltage arcs transfer very little noise power into the antenna. Beverages are thus quite resistant to precipitation static.

## Slide 11: Receive Loop Antennas

## Slide 12
Max
Max
Null
Null
Diagram from Joseph Carr’s
Practical Antenna Handbook
Notes: Unlike a large loop antenna (greater than 0.5 wavelength), a Receive Loop is much smaller (most are less than 0.1 wavelength), and exhibits a much different antenna pattern. RX Loops deliver strongest signals in the direction of the plane of the loop, and sharp nulls broadside to that plane.
Signals broadside to the loop induce the same voltage throughout the wire of the loop. Because all sections of the wire are at the same potential, no current can flow. Signals off the ends of the loop induce different voltages in the loop wire as they travel through it, allowing a current to flow.
The advantage of the RX Loop is the sharp null. Careful positioning can block out an interfering signal or noise, and permit the desired signal to be heard.

## Slide 13
Notes: A typical homebrew RX Loop. Note the use of a separate loop inside the main winding. It presents a better impedance match to the receiver. It also prevents the main loop from being too heavily loaded by the receiver. This would destroy the Q of the circuit, allowing strong, off-frequency signals to enter the receiver’s front end.

## Slide 14
Normal loop in free space
Nulls “filled in” by nearby metal objects
Diagram from Joseph Carr’s
Practical Antenna Handbook
Notes: The presence of metal objects near a loop antenna can upset the balance of the system, causing the null to “fill in”. This sort of distortion can eliminate the advantage of an RX loop – the sharp null that can be used to block an interfering signal or noise.

## Slide 15
Diagram from Joseph Carr’s
Practical Antenna Handbook
Notes: This can be eliminated by shielding the loop as shown. This ensures that the loop remains balanced with respect to ground despite the presence of nearby metal objects. It has nothing to do with receiving the magnetic component of an EM wave – this is a common misconception! Check out the website of W8JI (www.w8ji.com) for an in-depth explanation. In reality, the shield becomes the actual antenna, not the wire inside the loop. There are many good and bad ways to feed and shield an RX Loop. Points to remember:
The shield is the actual antenna
The shield must be perfectly symmetrical away from the inner wire exit point
The gap in the shield must be exactly opposite the grounded point
The ground must be at the inner wire exit point
The shield will not make an unshielded loop that is properly balanced any quieter
The shield only is a tool to help you balance the system IF the shield is properly implemented

## Slide 16
Diagram from Joseph Carr’s
Practical Antenna Handbook
Notes: RX Loops mounted in the shack can be tuned manually with variable capacitors. Tuning remote loops can be more problematic. I have tried slow speed electric motors to turn the variable capacitor. The electric noise from the motor makes it difficult to peak the antenna. Varactor Diodes, which exhibit a changing capacitance as the voltage is varied, can be used instead. The voltage is fed up the coax, using a DC blocking capacitor to protect the receiver.

## Slide 17
Diagram from Joseph Carr’s
Practical Antenna Handbook
Notes: You can use a feedback loop to increase the gain and the Q of the loop. This circuit is essentially an Armstrong oscillator that doesn’t quite oscillate. The signal provided by the feedback loop must be adjusted until the circuit is on the verge of oscillating. At that point, the gain increases and the bandwith narrows. It takes some skill to use this type of RX Loop, but it is apparently an excellent accessory. Some sort of potentiometer might be necessary to better control the amount of feedback.

## Slide 18: Receive Loops Summary
Pros
  Small, lightweight
  Easy to build
  Sharp null in 2 directions
Cons
  Poor sensitivity
  Broad RX pattern
  Often next to noise source in shack
Receive loops can be a useful tool in some
situations, but are probably better suited for
SWL and BCB/LF Beacon DX’ing.
Notes: Because of the poor sensitivity compared to many other RX antennas, RX Loops are probably better suited for SWL, Broadcast Band and LF Beacon DX’ing, where signals are going to be stronger than on the Amateur bands.

## Slide 19: Elongated Terminated Loops
Include Ewe, Flag, Pennant and K9AY
Terminated loop produces a cardioid pattern
Depth and angle of null depend on loop shape

## Slide 20: Theory of Operation
Despite the shape, actually a pair of verticals
Feedline on top and bottom gives crossfire phasing towards feedpoint when elements closer than ¼ Lambda
Terminating resistor is equal to feedpoint impedance, and ensures equal current throughout
Thus, vertical elements have phase difference of 180 deg plus electrical length of connecting wires (slightly more than element spacing)
This gives the cardioid pattern
Terminating Resistor
Coax
Matching X’fmer
Direction of Reception
Notes: These elongated terminated loops are really a simple pair of verticals with a horizontal feed line, one being basefed, the other being fed via the top wire. That provides crossfire phasing. When the element spacing is less than λ/4, this always fires towards the feed point end of the array. When properly terminated the loops show nearly constant current at all points on the loop. This constant current is achieved by terminating the far end of the loop in the same impedance as the feed point. Thus, the portions considered to be the vertical “elements” have equal current, with a phase equal to 180° plus the electrical length of the connecting wires, which is slightly more than the element spacing.
In other words, the terminated loop is like two constant current verticals with classic end-fire phasing. The only difference is the horizontal component in the radiation due to the radiating delay line (sloping or horizontal) of the terminated loops. This is the operating principle for the entire family of elongated terminated loops. Sloping (inclined) wires used in some of the designs are just like a horizontal wire in combination with a vertical wire, and the same reasoning as above can be used.

## Slide 21
Ewe Antenna
Diagram from ON4UN’s
Low Band DXing
Notes: Floyd Koontz, WA2WVL, is the originator of the EWE. His QST articles are must-reads on this novel receiving antenna. Incidentally, the curious name “EWE” came about because Floyd noted that his new antenna looked very much like an upside-down letter “U.” He jokingly submitted a drawing of a female sheep—a ewe—to headline his February 1995 QST article, which he impishly titled with the triple entendre “Is This EWE for You?”
A EWE is small, requires little engineering, and can be designed to cover 80 and 160 meters. Moreover, the EWE is low profile and can be built for little money. In appearance, the EWE resembles a very short Beverage, though in fact it as an array of two short vertical antennas.
The horizontal wire is only about 5 to 15 meters long and is about 3 to 6 meters above ground. In other words, an EWE can fit in many tiny yards. The original description by WA2WVL uses 3-meter high “elements” with a spacing going from 4.5 to 18 meters, depending on the band (80 or 160 meters).
A good rule of thumb is to build an EWE where the length is twice the height. This rule can be followed for elements going from 3 to 6 meters in height, and will result in an optimum termination resistance of approximately 1000 Ω for both bands. The smaller the array, the easier it is to obtain a good deep null, but the lower the output level. The larger versions will be near the cut-off frequency, where a deep null cannot be obtained.
The output (gain) of the antenna depends on its size. The gain for 160 meters varies typically between –20 dBi and –30 dBi over average ground, and is about 9 dB higher on 80 meters. The inverted-V shaped EWEs looks quite attractive and can easily be made into a “hand-rotatable” receiving antenna: Just walk out in the garden and anchor the sloping wires to a different set of ground rods. It should be useful for DXpeditions as well.
The value of the terminating resistor is quite critical if you want to obtain a good notch in the back response. Since the ground resistance is part of the terminating resistance, a good low-impedance, stable ground is required. The ground resistance of a single ground rod may vary from as low as 50 Ω to as much as several hundred Ω. Although the terminating resistance is high (typically 1000 Ω), a ground consisting of more than one ground rod or a combination of a ground rod with various short radials is a good idea.

## Slide 22
Ewe Antenna at KC4HW
Notes: Ewe Antenna at KC4HW
It has been reported that the best way to tune an array for best F/B is to find a medium-wave BC transmitter in the back of the antenna. Using a medium-wave signal during day time ensures that you will receive it on ground-wave, and as such have a constant and stable signal source. Tune the terminating resistor for a full notch, striving for a minimum of 25 dB. This value will be very close to the best value for 160 meters and close to what’s best on 80 meters.
You should use broadcast stations between 1600 and 1700 kHz to do the null adjustment if you can. It is impossible to reliably adjust the termination resistance using signals arriving by skywave. You could also use a nearby local ham (in-line off the back) or set up a small signal generator off the back, using a small vertically polarized antenna, at a distance of at least 1 λ from the EWE (which means outside its near field).

## Slide 23
Flag Antenna
Diagram from ON4UN’s
Low Band DXing
Notes: A major drawback to the EWE is its extreme sensitivity to any change in the local soil conductivity. EA3VY was the first to come up with the idea of adding a ground wire between the bottom of the two verticals as an effective way to minimize the effect of different soil conductivities.
Many dimensions will work but only the optimized ones provide the best directivity over the largest frequency range with a single termination resistor. These standard values developed by EA3VY and K6SE are 4.27 meter (14 feet) high by 8.84 meters (29 feet) wide, with a bottom wire height of 2 meters (6 feet) above ground. These dimensions result in an antenna that has excellent characteristics from 7.5 MHz down.
This configuration has a gain of approximately −28 dBi on 160 meters, −18 dBi on 80 meters and –10 dBi on 40 meters. The loop is terminated with 950 Ω and fed in the centers of opposite vertical sections. Its input impedance on 160 meters is 950 Ω with a small reactive component (10 to 50 Ω).
A properly designed Flag exhibits a high F/B ratio over any type of soil and at virtually any height above ground without need to change the dimensions or termination value.
K6SE, who has thoroughly tested all shapes and sizes of elongated terminated loop antennas, reports that the Flag antenna is probably the best of all configurations from the standpoint of being broadbanded and having gain. It has about 6 dB more gain than an equal-sized Pennant.

## Slide 24
www.qsl.net/w7iuv/
Notes: The shape and the size of this loop makes it attractive for a rotatable version. W7IUV describes such a design on his website (www.qsl.net/w7iuv/).

## Slide 25
Pennant Antenna
Diagram from ON4UN’s
Low Band DXing
Notes: While optimizing the flag, K6SE and EA3VY developed the triangular-shaped loop. He named it the Pennant because its triangular shape resembles a flag pennant. The loop is fed in the center of the vertical section, while the load is situated where the sloping wires meet.
The correct termination resistor for the Pennant is about 900 Ω, which can be placed either at the point of the Pennant or in the center of the vertical section—the results are identical. The feed point is at the opposite end. Gain on 160 meters is about –34 dBi (which is 6 dB less than the Flag), −24 dBi on 80 meters and –16 dBi on 40 meters. The exact values depend on local ground conductivity. Note that the 6-dB lower signal level is proportional to the difference in area enclosed by the loop, which is half as much as the Flag: 1/2 voltage = 1/4 power (−6 dB).

## Slide 26
Delta Ewe Antenna
Diagram from ON4UN’s
Low Band DXing
Notes:         A EWE in the shape of a Delta loop has every bit as clean a pattern as the more classic ones. I think this antenna is really attractive for DXpeditions and for semi-rotatable setups. Just moving the base line around is all you have to do to change directions. During modeling it appeared that the best F/B was obtained with the terminating resistor mounted approximately 20% from the bottom corner of the Delta loop. The antenna is fed in the opposite bottom corner.
        The FOØAAA Clipperton Island DXpedition used this antenna in their operation. It is the only design that requires only one support and can be easily rotated manually, a very desirable feature for DXpedition use. The Clipperton team found the antenna to be very successful and many other subsequent DXpeditions have also used the Delta configuration.
        The optimum termination resistance for this design is also 950 Ω. The antenna was optimized for 160 meters and its output is about –33 dBi on 160 meters, −22 dBi on 80 and –13 dBi on 40 meters.

## Slide 27
K9AY Antenna
Diagram from ON4UN’s
Low Band DXing
Notes:         Gary Breed, K9AY, described this loop very well in his Sep 1997 QST article (Ref 1265). This is another variant of the EWE, where the bottom wire of the loop is grounded in the center. See Fig 7-128. He pointed out in his article that the loop can really be any shape. The diamond shape K9AY used was dictated by practical construction considerations rather than anything else. All of the K9AY loops can be used on both 160 and 80 meters, although optimal performance may require slight adjustment of the terminating resistance, as K9AY pointed out in his article.
        While in all the previously described loops the feed point and the termination are separated by distance (they are at opposite ends of the elongated loops), in the K9AY loop “separation” is achieved by grounding the loop between the adjacent feed and termination points. Having the feed and termination so close to one another makes it easy to switch directions from a single box.

## Slide 28
http://www.hard-core-dx.com/
Notes: Using the proper relay switching setup, it is possible to insert the matching transformer and termination relay as necessary so that 4 different directions can be selected.

## Slide 29
http://www.hard-core-dx.com/

## Slide 30
K9AY Switchbox
Diagram from ON4UN’s
Low Band DXing

## Slide 31
K9AY Control Box
Diagram from ON4UN’s
Low Band DXing

## Slide 32
Ground
Diagram from ON4UN’s
Low Band DXing

## Slide 33
Photo from ON4UN’s
Low Band DXing
Notes: K9AY offered by AY Technologies.

## Slide 34
Diagram from ON4UN’s
Low Band DXing
Notes: K9AY has a much smaller footprint than 4 Ewes.

## Slide 35: Feeding Elongated Loops
Impedances range from 500 Ohms in K9AY, to 950 Ohms in Deltas and Flags.
Important characteristics:
  Lowest possible capacitive coupling between primary and secondary windings.
  Low loss, as signals are weak
  Good SWR if you want to phase loops into an array of loops
Notes:         The essential characteristics of a good transformer for a loop antenna are:
Lowest possible capacitance coupling between primary and secondary windings.
Low loss because signals are very low-level.
Good SWR is essential if you want to phase such antennas (you want the phase angle to be the determined by the cable length!)

## Slide 36
Transformation Low-Z High-Z
500 Ω to 75 Ω 2 passes (1 turn) 5 passes
500 Ω to 50 Ω 2 passes (1 turn) 6 passes
950 Ω to 75 Ω 2 passes (1 turn) 7 passes
950 Ω to 50 Ω 2 passes (1 turn) 9 passes
I use binocular cores made from
#73 material. Separate windings
ensure low coupling, and good
balance. Other designs are
possible.
Diagram from ON4UN’s
Low Band DXing
Notes:         Winding Data for Binocular Transformer
Transformation Low-Z High-Z
500 Ω to 75 Ω 2 passes (1 turn) 5 passes
500 Ω to 50 Ω 2 passes (1 turn) 6 passes
950 Ω to 75 Ω 2 passes (1 turn) 7 passes
950 Ω to 50 Ω 2 passes (1 turn) 9 passes

## Slide 37
Diagram from
www.w8ji.com
Notes:         Summing Up, Feeding Elongated Receiving Loops
- Make sure your loop is as physically balanced as possible.
- It’s better to have the loop 5 meters high than 2 meters.
- Use a transformer with separate primary and secondary windings.
- Use a transformer with the lowest possible capacitive coupling between primary and secondary windings.
- Do not use a metal box to house the transformer.
- Run the feed line along the symmetry axis of the loop for several meters.
- Drop the coax down to ground, where you ground the shield to a good ground system. Insert a common-mode
        choke at that point (between the ground rod and the shack).

## Slide 38: Elongated Loop Summary
Pros
  Small footprint
  Simplicity
  Can be phased to improve performance
  Much better than listening to a vertical!
Cons
  Insensitive, may require a preamp
  Directivity not as good as a Beverage
  Feedline prone to noise pickup
Although not as good as Beverage antennas,
Elongated Loops offer good performance
for people who don’t have much room.

## Slide 39: The Beverage Antenna!
Notes: Dr. Harold Henry "Bev" Beverage (14 Oct 1893 in North Haven, ME - 27 Jan 1993) is perhaps most widely known today for his invention and development of the wave antenna, which came to be known as the Beverage antenna and which for the last few decades has seen a resurgence in use within the amateur radio and broadcast DXing hobbyist communities. Less widely known (outside of the community of science history researchers) is that Bev was a pioneer of radio engineering and his engineering research paralleled the development of radio transmission technology throughout his professional career with significant contributions not only in the field of radio frequency antennas but also radio frequency propagation and systems engineering.
[edit] Biography
Harold Henry Beverage received a B.S. in Electrical Engineering from the University of Maine in 1915, and went to work for General Electric Company the following year as a radio-laboratory assistant to Dr. Ernst Alexanderson. In 1920, he was placed in charge of developing receivers for communications at the Radio Corporation of America in Riverhead, New York. Three years later, at the age of 30, he received the IRE Morris N. Liebmann Memorial Prize "for his work on directional antennas."
RCA named Beverage chief research engineer of communications in 1929, a position he held until 1940. At that time, he was promoted to vice president in charge of research and development at RCA Communications Inc., a subsidiary of the Radio Corporation of America. He retired in 1958 from that position and as director of radio research, but continued to work in communications as a consultant.
In 1938, the Radio Club of America presented him with its Armstrong Medal for his work in the development of . The Beverage antenna, the citation said, was "the precursor of wave antennas of all types." Beverage was awarded the IRE Medal of Honor in 1945, "In recognition of his achievements in radio research and invention, of his practical applications of engineering developments that greatly extended and increased the efficiency of domestic and world-wide radio communications and of his devotion to the affairs of the Institute of Radio Engineers."[1] In awarding him its Lamme Medal in 1956 the American Institute of Electrical Engineers cited him "for his pioneering and outstanding engineering achievements in the conception and application of principles basic to progress in national and worldwide radio communications."
Mr. Beverage died on 27 January 1993 at the John T. Mather Hospital in Port Jefferson, L.I. He was 99, and lived in Stony Brook, New York.

## Slide 40
Notes: Harold Beverage discovered in 1920 that an otherwise nearly bidirectional long wire antenna becomes unidirectional by placing it close to the lossy earth and by terminating one end of the wire with a non-inductive resistor with a resistance approximately matched to the surge impedance of the antenna. This was the fundamental discovery in his 1921 patent.

## Slide 41
Diagram from Joseph Carr’s
Practical Antenna Handbook
Notes: The Beverage Antenna relies on "wave tilt" for its directive properties. At low and medium frequencies, a vertically polarised radio frequency electromagnetic wave travelling close to the surface of the earth with finite ground conductivity sustains a loss that produces an electric field component parallel to the earth's surface. If a wire is placed close to the earth and approximately at a right angle to the wave front, the incident wave generates RF currents travelling along the wire, propagating from the near end of the wire to the far end of the wire. The RF currents travelling along the wire add in phase and amplitude throughout the length of the wire, producing maximum signal strength at the far end of the antenna where a receiver is typically connected. RF signals arriving from the receiver-end of the wire also increase in strength as they travel to end of the antenna terminated in a resistor, where most of the energy propagating in that direction is absorbed.
Radio waves propagate by the ionosphere at medium or high frequencies (MF or HF) typically arrive at the earth's surface with wave tilts of approximately 5 to 45 degrees. Ionospheric wave tilt allows the directivity inducing mechanism described above to produce excellent directivity in Beverage antennas operated at MF or HF.
While Beverage antennas have excellent directivity, because they are close to lossy earth they do not produce absolute gain (typically -20 to -10 dBi). This is rarely a problem, because the antenna is used at frequencies where there are high levels of atmospheric radio noise. The antenna has very low radiation resistance (less than one ohm) and will rarely be utilised for transmitting. The Beverage antenna is a popular receiving antenna because it offers excellent directivity over a broad bandwidth, albeit with relatively large size.

## Slide 42: Influence of Length
Following slide shows EZNEC results for a Beverage with following characteristics:
  2 meters high
  Over good ground
  600 Ohm termination
  0.55 to 4.4 wavelength
  160 M band

## Slide 43
710 M
-4.0 dBi
4.4 wl
535 M
-4.7 dBi
3.3 wl
353 M
-6.3 dBi
2.2 wl
268 M
-7.6 dBi
1.68 wl
176 M
-9.9 dBi
1.1 wl
89 M
-14.3 dBi
.55 wl
Diagram from ON4UN’s
Low Band DXing
Notes: Note how the pattern sharpens, and gain increases as the length is increased. The lesson would seem to be that the longer the better for Beverage antennas. This is not true in actual practice however!

## Slide 44
Notes:         One limiting factor is the phase difference that will occur between the EM wave in free space, and the slower induced EM wave in the antenna. As the antenna is increased in length, that phase difference grows until the EM wave in free space is actually subtracting from the induced wave in the antenna. Of course, the slower the wave in the antenna (ie: the lower the velocity factor), the shorter the antenna will be before that point is reached.
        The velocity factor of a Beverage will vary typically from about 90% on 160 meters to 95% on 40 meters. These figures are for a height of 3.0 to 3.5 meters. At a 1-meter height the velocity factor can be significantly lower, depending on ground quality. BOGs (Beverages on ground) may have a velocity factor around 60%, which means that very short, very low Beverages can exhibit radiation patterns similar to higher Beverages that are much longer.
        This equation is used to calculate a maximum effective length based on the velocity factor. If we use a VF of 90% for a 160M Beverage (assuming 3 meters above the ground), then the MEL is 360 meters, or 2.25 Lamda. For a wire laying on the ground with a VF of 60%, the MEL is 60 meters, or 0.375 Lamda.
        Even before this MEL limit is reached in antennas with a high VF however, there is another limiting factor. There is such thing as space diversity, which means that wave characteristics change with place. As long as you stay within a radius of approximately two wavelengths, this usually does not cause any problems. This is the reason why very large arrays and very long Beverages, may actually behave differently from what the model tells us. “Longer is better” does not hold true for Beverages (as for any large receiving array). Besides, we have already seen that gain is not an important factor in RX antennas – directivity is.

## Slide 45: How High?
Not as critical as many think
General rule:
  Higher Beverages produce higher output
  Higher Beverages have larger side-lobes
  Higher Beverages have a higher elevation angle
  Higher Beverages have a wider 3-dB forward lobe
Laying on ground to 6 meters high is acceptable
1.5 x Antler Height is good idea!
2.5 meters is a good compromise
Notes:         The general rule is as follows:
- Higher Beverages produce higher output
- Higher Beverages have larger side-lobes
- Higher Beverages have a higher elevation angle
- Higher Beverages have a wider 3-dB forward lobe
        The height is not all that critical. Below 2 meters, Beverages can be a hazard for men and animals. If you must cross a driveway or small street, you can put your Beverage up to 6 meters high and still have a working Beverage. You can also slope the Beverage gently up from 2 meters to 6 meters to cross the obstacle without much harm at all. Tom, W8JI, writes on his Web page (www.w8ji.com): “I’ve found very little performance difference with height, unless the Beverage is more than 0.05 λ high.”
        If the Beverage can be constructed on terrain that is inaccessible to people, deer and other animals, then you can consider using Beverages at a height of 0.5 or 1 meters for added high-angle discrimination and reduced omnidirectional pick up.

## Slide 46: Ground Quality
The better the ground, the lower the output
Ground quality has little impact on radiation angle
The poorer the ground, the less pronounced the nulls between the different lobes
Directivity remains almost constant
Beverage does not work well over salt water
Notes:         - The better the ground, the lower the output from the antenna (around 6 to 8 dB difference between very poor ground and very good ground). But even over very good ground Beverages have more than enough gain.
        - The peak elevation angle changes only slightly with ground quality. For example, a 300-meter long Beverage peaks at 27° over Very Poor Ground. The response at 10° elevation is down 3.4 dB from the peak. Over Very Good ground, the lobe peaks at 29°, and the response at a 10° elevation angle is down 2.8 dB from the peak response.
        - The poorer the ground quality, the less pronounced the nulls will be between the different lobes. This is similar to what we notice with horizontally polarized antennas over real ground.
        - The directivity factors (DMF and RDF) of a Beverage antenna remains almost constant for grounds ranging from Very Good to Very Poor.
        - The Beverage does not work at all over sea water. Its output is down 15 dB compared to the same antenna over poor ground and the main elevation angle is at 45°. This confirms the observations made by Ben Moeller, OZ8BV, that his Beverages near the sea never worked well at all.

## Slide 47
Gain Curves
Radiation Angle Curve
Gain and Radiation Angle
Diagram from ON4UN’s
Low Band DXing
Notes: The elevation angle: The radiation angle only changes marginally (a few degrees) between very poor ground and very good ground. The elevation angles shown in Fig 7-67 are for Average Ground. Note the large difference in elevation angle between long and short Beverages: 17° for a 3-λ long antenna and approximately 40° for a 1-λ long antenna!
Gain: Fig 7-68 shows gain curves vs length, over very poor ground, average ground and very good ground. As indicated above, the gain figures may be a little optimistic, a known flaw with NEC-2 for antennas close to the ground. From these curves it may seem that maximum usable length is determined by the way gain diminishes beyond a certain length. This is not important because gain is not an important parameter with receiving antennas.

## Slide 48: Wire
Inefficient antenna anyway, so size not critical as long as it is physically strong enough
Insulated, not insulated – doesn’t matter
Pre-stretch soft-drawn copper wire
Copper-clad and aluminum wire also okay
Notes: - Insulated wire may be better if antenna can rub against tree branches. Insulation can also hide a broken conductor.
Long spans may be necessary, so pre-stretch soft-drawn copper wire.
Multi-conductor wire fine – solder ends together and use all conductors.

## Slide 49: Theoretical Surge Impedance
Z = 138 log
4h
d
Where:
h = height of wire
d = wire diameter (in same units)
Notes:         The theoretical impedance values calculated using this formula assume perfect ground. They are useful for estimating the terminating resistor for a single-wire Beverage and for designing matching transformers and networks. Note that the impedance does not change drastically with height or wire size.
        Over real ground however, the surge impedance appears to be higher than over perfect ground. This is because the electrical ground is not the surface of the ground, but a little deeper. The following correction figures can be used:
        Good ground: +12%
        Average ground: +20%
        Very poor ground: +30%
        Typical values range from 300 Ohms for a Bev laid on the ground, to 650 Ohms for very thin wire at 5 meters height. Practical values are usually 450 to 500 Ohms.

## Slide 50: Termination Resistor
Should be non-inductive
Antenna will pick up TX power and lightning surges, so use 2 watt resistor
Metal Film and Carbon Film cannot handle surges
Use Carbon Composition
Use a Spark Gap
Photo from ON4UN’s
Low Band DXing
Notes:         Riki, 4X4NJ, described such a homemade spark gap: “The spark gap consists of heavy solid wires—about 10 AWG, soldered to teardrop terminals that are placed under the screws going to the antenna and ground. The ends of the wires are cut with “side cutters” leaving a nice “knife edge,” and I position the two edges very close to each other. A piece of paper makes a nice “feeler gauge” for this purpose. It is very effective, most simple, and negligible cost.”
        Photo is of K9DX Beverage termination. Using fuse clips allows resistors to be replaced easily if burnt out by nearby lightning strike.

## Slide 51
Photo from www.w8ji.com

## Slide 52
Diagram from ON4UN’s
Low Band DXing
Notes: Methods to terminate a Beverage antenna.
        Different terminating systems for Beverage antennas. The version at A suffers from stray pickup because of the vertical down lead. At C, two in-line quarter-wave lines terminate the Beverage, by which the radiation from these lines is effectively canceled. This is not a very practical solution because of its area requirements. This configuration is used through the book for modeling Beverage antennas, however. At D, the method most widely used with real-world Beverages. Using a long sloping section is thought by many to reduce omnidirectional pickup.
        In reality, vertical drop is vertical drop, no matter if it is over 20 meters, or straight down. If it weren’t, then the K9AY and similar antennas would not work!

## Slide 53: Supports
Metal, non-metallic – doesn’t matter as long as antenna is insulated
Poles, fence posts, trees, sheds, misbehaving children – whatever is available
Do not wrap wire around an insulator
Try to keep it straight and level, but minor variations are okay
Notes:         If the terrain is irregular, minor ups and downs in height or dips or valleys will not ruin your Beverage performance though. If your terrain is not flat, follow the contour of gradual slopes and go straight across ditches or narrow ravines without following the contour.

## Slide 55
Photo from ON4UN’s
Low Band DXing
Notes: PVC pipe with slot sawn in the top.

## Slide 56
Photo from www.w8ji.com
Notes: Recommended by W8JI
Try to have the wires able to slip through insulators. Easier to detect a wire break, and lessens the chance of the wire actually breaking.

## Slide 57
Photo from www.w8ji.com
Notes: Recommended by W8JI

## Slide 58
Photo from www.w8ji.com
Notes: Not recommended by W8JI (though I use the same type of standoff insulator!)

## Slide 59: Parallel and Crossing Beverages
Separate parallel Beverages by distance equal to their height above ground
Separate by at least 10 cm when crossing
Do not run close to parallel conductors (fences, telephone poles etc.)
Notes:         Parallel Beverages
        Beverages are non resonant and exhibit very little mutual coupling. The rule of thumb is to keep two parallel Beverages separated by a distance equal to their height above ground. This separation guarantees a decoupling of at least 30 dB.
        Crossing Beverages
        Beverage antennas for different directions may cross each other if the wires are separated by at least 10 cm (4 inches). Beverage antennas should also not be run in close proximity to parallel conductors such as fences, telephone lines, power lines (even if quiet) and the like.

## Slide 60
Photo from ON4UN’s
Low Band DXing

## Slide 62: Matching the Beverage Antenna
Several different core material/turns combinations available
Separate primary/secondary windings advisable
I prefer Type 73 Binocular Cores as recommended by W8JI
Notes: ON4UN has a discussion on the various matching transformers that could be employed. I prefer the binocular cores recommended by W8JI. Separate windings help prevent spurious signal pickup on the coax shield.

## Slide 63
Winding Binocular Cores
Pri Sec Pri Z Sec Z
Passes Passes Ohm Ohm
4 10 75 450
6 16 75 533
4 12 50 450
6 20 50 550
Note: Using Fair-Rite 2873000202
Binocular Cores (1 turn = 2 passes)
Diagram from ON4UN’s
Low Band DXing

## Slide 64: Coax
Can use 50 or 75 Ohm cable
I prefer 75 Ohm cable
  Works very well (ensure it is good quality cable)
  Cheap!
  Easy to attach connectors in the field
  Easily identifiable as part of RX system – will not accidentally transmit into it
  Did I mention that it is cheap?
Notes: - Even with inexpensive TV quality 75 Ohm cable, losses in runs of several hundred feet are acceptable.
Do not suspend coax – keep on ground to prevent signal pickup on shield.
Use flooded cable if critters a problem.
Use RF chokes to keep signals off shield - Five turns of miniature coax through a FT150A-F core (μ = 3000 and AL = 5000) achieves an impedance of 1500 Ω (7 turns = 3 kΩ on 160 meters).

## Slide 65: Grounds
One 8-foot ground rod may suffice
Will probably need two or more to stabilize the ground system
Can supplement it with a number of short radials to form capacitance hat to earth
On coax end of antenna, do not ground the coax braid
Ensure the coax braid ground is no closer than 5 meters to the ground attached to the transformer

## Slide 66
Multiple Beverages from one Hub
Diagram from ON4UN’s
Low Band DXing
Notes:         Make sure you always switch both the inner conductor and the shield of these feed lines. Do not connect the shields of all these feed lines together or to a common ground. If you want to ground them, do so at a distance of 5 meters from the switch box, to individual ground stakes that are well separated.
        If at all possible I suggest using widely separated end posts for the Beverages, with at least 5 meters separation and separate grounds (Fig 7-92E). Avoid using the antenna ground of one antenna as the termination ground of another one that might be running in the opposite direction.
        Little or no coupling occurs between the antenna wires, unless they are parallel and quite close together. I have not noticed any problem with antennas arriving at one point under a 30° angle.

## Slide 67
Two Directions from
one Beverage
Diagram from ON4UN’s
Low Band DXing
Notes:         At A, open-wire two-direction Beverage antenna. This uses reflecting transformers to obtain both reflections and proper impedance matching (see text for details). At B, an autotransformer is used for the same purposes.

## Slide 68
Another Method…
Diagram from ON4UN’s
Low Band DXing
Notes:         When the Beverage antenna is not terminated, the directivity will be essentially bi-directional. In real life the unterminated Beverage is not a true bi-directional antenna. The SWR and the loss on the antenna make it have some F/B. F/B is related to standing waves on the antenna; that is, to the reflection making it back to the receiver. Fig 7-95 shows the horizontal directivity pattern for a 1-λ long unterminated Beverage antenna. Notice the slight attenuation from the back direction because of the extra loss of the reflected wave in the wire.
        A method of switching the Beverage from unidirectional to bi-directional is shown in Fig 7-96. A relay at the far end of the antenna wire is powered through the antenna wire and the earth return via an RF choke and blocking capacitors.

## Slide 69: Phasing Beverage Antennas
To improve directivity without using long antennas, can phase individual Beverages
Two methods:
  Broadside
  End-Fire (or Staggered)
Each has its own advantages
Notes:         Can you really improve Beverages by phasing them? Theoretically you can achieve a narrow forward lobe (and hence a very high DMF) using a very long Beverage. To achieve the same 55° frontal lobe beamwidth as from an 8-Circle antenna (Section 1.30), you would need a 3-λ long Beverage (~550 meters on 160 meters), which poses two problems:
Not many have that much room for such long Beverages.
You run into space-diversity problems with this long an antenna, and you will never reach the results predicted by modeling.
        The only way to achieve a similarly narrow forward beam and hence a very high RDF is to use a broadside array of Beverages, exactly the same as what we did with short verticals in Section 1.11. You can obtain excellent results with shorter Beverages (1 to 2 λ long) but these require a broadside spacing of a little over λ/2. There is no free lunch!

## Slide 70: Broadside Phasing
Narrows frontal lobe
Front/Back remains the same
Fed in phase
Multiband
Require wide spacing
0.5 wl spacing good
0.67 wl excellent!
To RX
Splitter
Coax
Coax
Beverage
Beverage
0.5 to 0.67 wavelength
RX Direction
Notes: If the spacing is too wide, phase differences caused by space diversity will negatively impact directivity.

## Slide 71: End-Fire Phasing
Greatly improves Front/Back directivity
Front lobe remains much the same
Spacing 5 meters
Stagger NMT 0.5 wl
20 m for 40 – 160m ant
30 m if only 80 – 160m
Diagram from ON4UN’s
Low Band DXing
Notes: This method requires a phasing line, and is therefore limited to one band. There is a simpler method that permits multi-band use however.

## Slide 72
Photo from ON4UN’s
Low Band DXing
Notes: End-fire phased Beverages at W3LPL

## Slide 73
Broadside Phasing
End-Fire Phasing
Diagrams from ON4UN’s
Low Band DXing
Notes: Broadside Phasing - A single 160-meter long Beverage (solid line); two such Beverages in phase, side-by-side, spacing 40 meters (dashed line) and 90-meter spacing (slightly over λ/2, dotted line). Actual gain is irrelevant for receiving. Note very little little change in pattern with 40-meter spacing other than 3 dB improvement in gain (irrelevant for RX). With 90-meter spacing the frontal lobe is much sharper.
End-Fire Phasing - Azimuth pattern on 1.83 MHz for a single 320-meter Beverage (solid line); azimuth pattern for end-fire pair of 160-meter long Beverages, half the length (dashed line). Note that while gain is greater with the long single beverage, the side and rear lobes are very sharply reduced on the end-fire pair of shorter Beverages.

## Slide 74: Crossfire Phasing
Simple end-fire feed system developed by W8JI
Usable over several octaves
Termination value = twice that of single Bev
16:1 matching transformer used (900 Ohms)
(X – S)/2 = Y2
Y1 = X – Y2
Diagram from ON4UN’s
Low Band DXing
Notes:         Here is the W8JI’s description of the antenna: “Although it looks like a large horizontal loop, this antenna actually is an array of two ground-connection-independent end-fire staggered Beverages. The short end wires form two single-wire feed lines at each end. One end-wire is series terminated with exactly twice the resistance of a normal Beverage, while the short wire at the opposite end is the feed-point.
        Stagger and spacing determines feed and termination location, the offset at the two ends being mirror images. A top view, looking down from straight above the antenna is given in Fig 7-117.
        Notice the feed point is offset towards the termination end (front) of the antenna, and away from the null direction. This is typical for crossfire phased arrays. Crossfire arrays respond away from the delay line direction, exactly opposite conventional arrays. The termination is offset the same amount, but moves towards the feed-point end of the antenna.
        The feed-point terminals, being floated (push-pull), provide 180-degree phasing between the two elements. The extra line length to the forward (left and front) element provides the “Stagger” delay. Consider the actual wire length of a “short side” called “X” (which is the same as Y1+Y2). This length is the same on both ends of the antenna. The difference between Y1 and Y2 must equal or be slightly less than stagger (S).To determine the offset of feed point and load:
        1. Measure length of the end-wire, length “X.”
        2. Measure stagger in the end-fire direction, “S”
        3. (X − S)/2 = Y2
        4. Y1 = X − Y2
        Values used in ON4UN example: Stagger 21 meters, Y2 = 1 meter, Y2 = 21 meters
        Note that no ground is needed. Note also that the antenna is symmetrical – the feedpoint and termination resistor could be interchanged.

## Slide 75: Beverage Antennas at VO1NO/VE3
5 acres near Merrickville
Dimensions ~ 650 x 320 feet
8 directions using end-fire phased Beverages
Control Box in shack, with 3 switchboxes in field

## Slide 76
Notes: In the shack I have a control box with a knob surrounded by 8 LEDs. As the knob is rotated, a direction is selected, and the corresponding LED is illuminated. I have two coax cables running from the control box to three remote switchboxes in the field (one switchbox feeds into another), and coax running to the receive input on my rig. The switchboxes use relays to switch both the center conductor and braid of the coax to select the proper antenna i.e.: direction. Switching both conductors is important - directivity can be lost if this is not done. As a particular direction is chosen in the shack, the appropriate coax is selected, and the proper control lines energized so as to activate the required relays in the remote switchboxes. Also, 24VDC is applied to the center conductor of the coax that runs to the remote switchbox. More on that in a moment.
I use a Kenwood TS-950SD on HF. It has two RCA plugs on back – RX Ant Out and RX Ant In. Normally they are connected with a jumper, but they can also be used to connect a separate RX antenna. I run a cable from both to the control box. Using the knob in the lower right, I can connect the Beverage antennas, or several other RX antennas, including my K9AY. I can also bypass the RX antennas, feeding the RX Ant Out into the RX Ant In. This makes it easy to use other antennas when I go to higher bands.
The control box also takes a feed from the PTT line. When I transmit, a relay is keyed to ground the input from the active Beverage. It might not actually be needed, but better safe than sorry! There is also room for a pre-amp if I ever need one.
Why did I use 24VDC? I had lots of 24VDC relays and a 24 VDC power supply. It also suffers from less I2R losses in the control lines and coax center conductor.

## Slide 77
Notes: I use end-fire phased Beverages, using the crossfire phasing method. Because of the symmetry of the feedpoint and termination resistor, I can get two directions from each pair. Each end of the array is fed with 75 ohm cable. The antenna feedpoint at each end is connected to a terminating resistor through a relay in a termination box. As described in the previous paragraph, when a particular direction is chosen, the appropriate relays are activated to connect the coax from the proper antenna array to the coax running from the control box. When this happens, 24 VDC is present at the termination box at the end of the antenna. That voltage is used to activate a relay that switches the termination resistor out, and the matching transformer in. Voila - the receiver is now connected to a pair of staggered phased Beverage antennas! Of course, DC blocking capacitors are used in the appropriate locations in the termination boxes and control box.
I found a use for empty anti-perspirant containers! Spray painted to protect from UV radiation, they make great boxes for housing the terminating resistor, matching transformer, relay and associated circuitry. The bottom is left open to allow moisture to drain. Although not apparent in the photo, the termination boxes and coax switchboxes have LEDs to indicate when voltage is applied. This makes troubleshooting easier.
Most of this was put up in the winter, with 1 meter of snow on the ground! It will be tidied up this fall.

## Slide 78
Notes: I use 8-foot long 2x2 pieces of lumber, attached to shorter pieces driven into the ground. Supports at the 4 corners are backed up with guy lines. Note the coax coil RF choke. It needs several cores to increase the choking effect.

## Slide 79
North
000
(Asia, India)
180
(S. America)
Terminating resistor/
Matching Xfmr combo

## Slide 80
North
090 True
(Africa)
270 Deg
(W6, S Pacific)
Terminating resistor/
Matching Xfmr combo

## Slide 81
North
150 Deg
(Caribbean,
S America)
330 Deg
(Japan, W. Aus)
Terminating resistor/
Matching Xfmr combo

## Slide 82
North
045
(Europe, N. Africa)
225
(W. Coast, NZ)
Terminating resistor/
Matching Xfmr combo
Signal combiner
Notes: Unfortunately, the direction to Europe corresponds to the narrowest dimension of my property, about 320 feet. To improve performance here, I am broadside phasing two pairs of echelon phased Beverages i.e.: I have two sets of echelon phased Beverage pairs, spaced at 300 feet, and fed with equal lengths of coax into a signal combiner - a total of 4 Beverages for these two directions. I can also select just one pair of echelon phased antennas if necessary.

## Slide 83
North
Terminating resistor/
Matching Xfmr combo

## Slide 84: Property too small?
Try a BOG (Beverage On Ground)
  Termination ~ 200 to 300 Ohms
  Need a 4:1 matching transformer
  Use ferrite beads to decouple feedline
  May require a preamp
  Beverage’s first antennas were laid on the ground
Diagram from ON4UN’s
Low Band DXing

## Slide 85
Example of an urban beverage installation
Notes: Tell cat story!

## Slide 86: For more Information…
The “Bible”!!
Also check the website of Tom Rauch, W8JI:
  http://www.w8ji.com
Try the Topband Reflector as well:
  http://lists.contesting.com/_topband/
Joseph Carr’s book also has lots of good stuff.

## Slide 87: Questions?

## Slide 89
Notes: T1 is a 7-turn transformer tapped at 5 turns (1.4:1 turns ratio, 2:1 impedance ratio) step-down transformer. 73 material binocular cores are ideal for 100kHZ to 30MHz applications.
The magic T transformer is 5 to 10 turns of twisted pair wire through a 73 material binocular core. Configured as a center-tapped winding.
R1 is twice the expected load impedance. For 50- ohm systems use a 100 ohm resistor.

## Slide 91
Notes: I recorded the forward gain in two different ways. First, I measured the absolute maximum forward gain. As the Beverage becomes longer, the maximum gain always increased. But, the elevation (take-off) angle of maximum gain slowly drops, from 66 degrees to 18 degrees. In dBi, the gain goes from -18.53 dBi to -8.31 dBi. Now we can see why a Beverage is usually not used for transmitting. A half-wave dipole or quarter-wave vertical, even a poor one, probably has a positive gain with respect to an isotropic radiator. This is a difference of approximately 10 to 20 dB, which is a substantial difference.
I also measured the forward gain at a take-off angle of 21 degrees. I selected this angle because it is a typical DX angle.
At the 250 foot length, the maximum gain is -18.53 dBi. At that same length, the gain at a 21 degree take-off angle is -22.27 dBi. As the Beverage gets longer, the two curves slowly overlap, since the take-off angle of maximum gain drops to 21 degrees (and eventually goes under 21 degrees). For all practical purposes, the two curves start to overlap at approximately 1200 feet. At 1800 feet, the maximum gain is -8.31 dBi, at an elevation of 18 degrees.
As the antenna becomes even longer, the gain continues to increase, and the elevation angle continues to drop. The gain peaks at a length of 6000 feet. The gain at that length is -5.38 dBi, and the take-off angle is 9 degrees. 9 degrees may be too low of an angle for typical DX conditions. If we consider the gain at 21 degrees, the gain peaks at an antenna length of 2500 feet. The gain at that length, at 21 degrees take-off, is -7.82 dBi.
As we move from a 250 foot to 1800 foot Beverage, the gain at a typical DX take-off angle increases by approximately 14 dB. The gain increase is monotonic. Gain always increases, it never decreases, either at the maximum gain angle, or at 21 degrees.
As with the RDF, the rate of change of the gain slows down with increased antenna length. If we select a length so that we achieve one-half of the overall gain difference, that length would be 590 feet (-22.27 dBi + (14 dB/2) = -15.27 dBi).

## Slide 92
Notes: As the Beverage becomes longer, the angle of maximum gain monotonically drops. When the length is 250 feet, the take-off angle is 66 degrees, a high angle that is not usually useful for DX. Usual DX take-off angles range between 10 and 30 degrees.
The first thing we notice about this graph is that it is not continuous, but steps in units of 3 degrees. This is due to the simulation parameters, and the selection of the angular spacing in the three-dimensional grid (EZNEC step size). In other words, this graph is an approximation of the real data. Samples are computed every 3 degrees. If you draw a smooth curve through this graph you will have the actual elevation angle.
As we have seen before, the rate of change is faster at shorter antenna lengths. The half-way point between 66 degrees and 18 degrees is 42 degrees. The take-off angle reaches 42 degrees when the antenna is 570 feet long.
The elevation angle continues to drop as the Beverage becomes longer. At a length of 8000 feet, the take-off angle is 6 degrees. It clearly cannot go below 0 degrees, and I do not know if it stops before 0 degrees.

## Slide 93
Notes: The 3 dB beamwidth is a measure of the size of the forward lobe in the azimuth plane. It is an angle, measured in degrees, and is the angle necessary for the maximum gain to fall off by 3 dB in each direction
The beamwidth starts off quite wide, 215 degrees for a 250 foot long Beverage. The beamwidth drops to 43.2 degrees for an 1800 foot Beverage.
It is interesting to note that unlike all previously presented measurements, which changed monotonically, the reported beamwidth does actually back up a few degrees from time to time. These are the very small spikes on the graph. I do not know if this is a true characteristic of the antenna, or, some artifact of modeling and simulation. I would tend to believe the latter.
It is also possible to measure the 3 dB beamwidth in the elevation plane. Although I did not record that data, the trend is the same as for the azimuth plane. The lobe narrows as the antenna becomes longer. If you combine the azimuth and elevation beamwidths with the take-off angle, the picture that emerges is of a rather large front lobe that both narrows and tips down as the antenna becomes longer.

## Slide 97
Notes: K9AY antenna at W8WWW